## Slide 1: Work in progress research
R. Taranovs, V. Jesilevskis, G. Miezitis, D. Bliznjuks, E. Klavins, A. Kalnins, V. Zagursky
An approach for meeting room activity monitoring and analysis

## Slide 2: The General Motivations of the Proposed Approach
General motivation — enhancing quality and efficiency of meeting room usage.
Motivations:
The need of unified and open platform for human occupied rooms’ environment monitoring;
Existing solution are proprietary, have limited functionality and sometimes are not scalable.

## Slide 3: The General Motivations of the Proposed Approach
Tasks:
Create scalable and open solution;
Provide user friendly graphical interface;
Eliminate system configuring for end users;
Increase system availability by using cloud based solutions.

## Slide 4: A Full-Solution Architecture
Capabilities:
Foundation layer for “Smart Offices” solutions
Simple WEB UI
Cloud Powered Backend API for unlimited scaling and storage
Vendor tolerant Configuration and common gateway

## Slide 5: RTU Part’s WSN Architecture
Legend:
SN – Sensor Node
ZR – ZigBee Router
ZC – ZigBee Concentrator
zED – ZigBee End Device
GW – Gateway
Cust-MAC – Custom Medium Access Control Protocol

## Slide 6: IoT Tasks Solved by Custom WSN
Micro-climate in the office and especially in meeting rooms:
  Humidity sensors.
  Temperature sensors.
Air quality monitoring:
  CO2 saturation sensor.
Presence detection:
  Based on PIR sensors.
Energy-efficient meeting rooms:
  Light intensity sensors allow:
    Detects if light is switched-on in empty room.
    Helps to define necessary amount of light in the meeting room.

## Slide 7: CO2 effects on humans

## Slide 8: CO2 concentration in RTU classroom
Chart: Time (min)

## Slide 9: Existing systems
Typical applications
  Environment for device (e.g. server) protection.
  Indoor air quality.
  Ventilation system monitoring.
  Noise measurement.
Systems in developement:
  Tyndall BEEM – energy consumption, light, temperature, humidity.
  Smart Sensor System for Ergonomic Assessment of Working Environment – temperature, humidity, light and noise.
  BMWSN – temperature, humidity, light, human detection.
  Handheld devices – e.g. IEQ Chek – temperature, humidity, CO2.

## Slide 10: Custom WSN Advantages vs. Proprietary Solutions
No | Custom-WSN solution | Proprietary solution
Usability | Flexible amount of SNs in a room | Use-cases are pre-defined.
Sensor variety | Different sensors’ utilization for monitoring purposes | Static sensor-wise solutions.
Protocol stack | Communication protocols can be chosen according to current task. | Solutions are designed for particular tasks and can be reused in other circumstances with possible limitations.
Integration | Fast integration with other systems. | Pre-developed API as integration and access interface.
Costs | Reduced costs due to cheaper hardware. | Higher, because of already produced hardware and software.
Development time | Longer. | Shorter to longer if additional features must be implemented.

## Slide 11: WSN Protocol Stack. Physical Layer
Physical layer:
  Nordic Semi PHY radio chip selected.
  Automatic re-transmission on PHY layer via pipe mechanism.

## Slide 12: WSN Protocol Stack. Data Link Layer
MAC&LLC layer:
  IEEE 802.15.4 MAC-like protocol but with smaller memory footprint.
  Link quality indicators are placed in MAC packet.
  LLC layer enables error control.

## Slide 13: WSN Protocol Stack. Networking Layer
Networking layer:
  At phase 1 a flooding-type protocol is proposed.
  As next an AODV type protocol should be provided.

## Slide 14: WSN Protocol Stack. Application Layer
Application layer:
  Is responsible for detecting sensors onboard of SN.
  Provide SN’s self-location procedure.
  Elliptic-curve based cryptography of sent data.

## Slide 15: Gateway as a Coordinator and Cloud Interface
Gateway tasks:
  Serves as protocol translator from WSN to TCP/IP networks.
  Provides interface to Cloud-Computing service. Here Windows Azure.
  Configure and coordinate elements across its WSN.
  Aggregate and pre-process sensorial data from WSN:
    Sends data to the Cloud server according to aggregation algorithm.
    May do some data-processing if requested.

## Slide 16: Next Research Topics
Communication protocol stack enhancement with energy-aware features for Data Link, Networking and Application layers.
Location procedure establishment with better precision.
Continue security-related studies.
Enhance IoT solution with wearables technology, like Goolge glass.